## Slide 2
Futuristic view of C4I systems in civil and defense -- Requirements and road map

## Slide 3: Sequence
Command, Control, Communications, Computer & Intelligence (C4I)
Tenets of C4I
Network-Centric Warfare
Communication and its Medium
Comparison of Transmission Bands
Role of Satellite Systems for Supporting C4I Infrastructure
Advantages & Disadvantages of Ka-band
Regenerative Satellites
Conclusion

## Slide 4: Command, Control, Communications, Computer & Intelligence (C4I) in Military Applications
The acronym C4I stands for "command, control, communications, computers, and intelligence“.
The Strategic Vision for C4I is to provide capabilities that enable forces to generate, use, and share the information necessary to survive and succeed on every mission.
One important capability that C4I systems provide commanders is situational awareness—information about the location and status of enemy and friendly forces.
What Is C4I?

## Slide 5: Command, Control, Communications, Computer & Intelligence (C4I)
Command and Control (C2) -The exercise of authority and direction by a properly designated commander over assigned and attached forces in the accomplishment of the mission
Communications - Communications network is the key enabler of C4I that transports information between all tiers of the battlefield
Computers - Support C2 and intelligence by processing information for achieving desired objectives
Intelligence (I) - Information and knowledge about an adversary obtained through observation, investigation, analysis, or understanding.

## Slide 6: Command, Control, Communications, Computer & Intelligence (C4I)
Command & Control
Computers
Intelligence
Communication
Sensors
Weapons
Battle Field Management System
Air Defense Surveillance Sys
Radio Links
O/F Networks
SATCOM
Integration,
Processing,
Correlation of Info
AEW
Ground Radar
EW System
UAV
Fighter Aircraft
Missiles
Ground Troops

## Slide 7: Command, Control, Communications, Computer & Intelligence (C4I) Architecture
AOC
SOC
BOC
GES
GES
Link 11
VHF
UHF
UHF
Remote Workstation
PABX
ADOC
Missiles
LRR
HF
External Services
C4I Secure Network
Link-16
GSS
RECON

## Slide 8: Command, Control, Communications, Computer & Intelligence (C4I)
Command & Control | Communications | Computers | Intelligence
Processed information to support decision making | Transportation of information amongst all levels | Processing information for achieving desired objectives | Information gathering through observation, analysis
Decision Support Systems Battle Field Management System Air Defense Surveillance System | Voice and Data Networks Radio Links O/F Networks Satellite Communications | Integration, Processing, Correlation of gathered information | Sensors AEW Ground Radar EW System UAV

## Slide 9: Tenets of C4I
The tenets of C4I are:_
A robustly networked force improves information sharing.
Information sharing and collaboration enhance the quality of information and shared situational awareness.
Shared situational awareness enables self-synchronization.
These, in turn, dramatically increase mission effectiveness.
The above capabilities are accomplished by a Reliable and Secure Communications Network.

## Slide 10: Network Centric Warfare as a New Trend in C4I Applications
An emerging theory of war in the Information Age
Using information sharing to gain competitive edge
Increased shared situational awareness relying on computation and networked communications technology
Enhanced speed of command
Networking sensors, decision makers, and shooters
  to increases synergy for command and control, resulting in superior decision-making for an overwhelming war-fighting advantage.
10

## Slide 11: C4I
Sensor
Operator
System
(Radar)
Decision Maker
System
(Combined Operational Picture)
Shooter
Operator
System
(Aircraft)
Comm
NCW
Comm

## Slide 12: Advantages of NCW
Some military advantages that are expected from applying NCW systems to military operations include the following:
To achieve shared awareness,
Increased speed of command,
High tempo of operations,
Greater lethality,
Increased survivability, and
A high degree of self-synchronization.
The key principle of network centric operations is that: providing a superior level of integration among separate systems by allowing every user gets all the needed information in the correct format and in timely manner to achieve Interoperability and superior decision-making.
12

## Slide 13: Network Centric Warfare – As a Dynamic Autonomous Digital Battlefield
UAV
RAH
Robotic
Sensor
NLOS
NLOS/BLOS
Infantry
Fighting
Vehicle
CDR/C2
RECON
UAV
NLOS
LOS/BLOS
NLOS
LAM/PAM
Joint Air Support
JSTAR
Robotic
Sensor
MUGS
UAV
UAV
Theater TOC
Airborne TOC
Field TOC

## Slide 14: Role and Importance of Communications in C4I
C4I is about networking and cannot survive without effective communication means.
Communication provides essential linkages to war system at every level of operation.
The importance of communication in C4I makes it our primary center of gravity for opponents to exploit our warfare capability
Communication - is the heart beat of C4I systems

## Slide 15: Challenges concerning the deployment of C4I Systems
Communication challenges:
  Interoperability: no seamless and dynamic interoperation between C4I nodes.
  Protocols Mismatched: no exchange of relevant information due to lack of consistent format.
  Different Software: versions and releases between C4I nodes are not the same
  Different Operating Systems
  Obsolescence in Technology: hardware and software
  Integration of New technology with legacy systems
  QOS Requirements
  Bandwidth limitation due to type of Medium and Service locations
15

## Slide 16: Comparison between Communication Media
 | Wireline | OFC | MW | Satellite
Bandwidth | Low | Max | Limited | Moderate in Ka Low in C&Ku
Deployment | Difficult (subject to terrain & distance) | Difficult (subject to terrain) | Easier (subject to distance) | Easiest (independent)
Geographical Range | Limited | Limited | Limited (LOS) | Unlimited (BLOS)
Mobility | Poor | Poor | Moderate | High
Propagation Delay | Low | Low | Low | High
Flexibility | Poor | Poor | Moderate | High
Susceptibility to ECM | Moderate | Very Low | High | High

## Slide 17: Advantages of Satellite System to C4I
Provides high mobility and quick deployment (Tactical operations)
Wide geographical coverage (Remote Locations)
Installation and running costs are independent of distance (Budgetary)
Independent of terrestrial infrastructure (Flexibility)
Maintenance free medium (Reliability)

## Slide 18: Disadvantages of Satellite Systems
Limited BW compared to fiber networks (Transponders and Power Limitation)
Propagation delay (Effect on Encryption and Synchronization)
Susceptibility to ECM and Threat Access (Interception, Jamming, Spoofing or Cyber Attack)
Dependence on weather (Rain (Fading)

## Slide 19: Satellite Transmission Bands
Frequency Band | Downlink | Uplink
C | 3.7 – 4.2 GHz | 5.925 - 6.425 GHz
Ku | 11.7-12.2 GHz | 14.0-14.5 GHz
Ka | 17.7-21.2 GHz | 27.5-31.0 GHz
X-band is not considered due to complexity of equipment for this purpose.

## Slide 20: Comparison between Satellite Bands
Frequency Band | Throughput/ VSAT | Antenna Size | Coverage | Propagation Delay | Rain Fade
C | 0.1–0.5 Mbps | Large | Global | 0.5 sec | Low
Ku | 2-6 Mbps | Small | Wide Beam | 0.5 sec | High
Ka | 8-20 Mbps | Smaller | Spot Beam | 1.0 sec (due to Double Hop) | Higher
Advantages
Disadvantages
Ka-band is the current trend in Satellite Communications due to other bands are becoming saturated

## Slide 21: Wide Beam Propagation : C & Ku Bands
SATCOM
Information travels to a site in a Single Hop

## Slide 22: Ka-band: Multiple Spot Beams
Beam 1
SATCOM
Beam 2
Beam 3
Beam 4

## Slide 23: Ka-band: Spot Beams Satellites
Typical Satellite acts as a repeater station in the space.
Spot beam satellites provide fixed data channel to communicate between different beams.
It can be said that communication channels between beams are hard wired. This is called the Bent Pipe Architecture
Therefore all the data received from various users by the satellite is transmitted to the Satellite HUB station and then re-transmitted to the desired destination by the satellite (double Hop architecture)
Steerable beams allows more flexibility with respect to Coverage areas.

## Slide 24: Bent Pipe Satellites

## Slide 25: Spot Beam Propagation : Ka-band
Transmission A B
Site A
Site B
Hub Station
SATCOM
Information travels from site to site in a Double Hop

## Slide 26: Advantages of Ka-band over other Bands
Greater throughput
More potential: currently widely used as lower bands such as C/ Ku become more congested
Spot Beam –
  Enables Frequency re-use as explained in upcoming slide
  Less susceptible to interception and jamming
High Mobility - smaller dish size
Some Disadvantages of Ka-band
Propagation Delay – Double hop due to Bent pipe architecture
Rain Fading - Due to absorption of high frequency electromagnetic waves by water droplets

## Slide 27: Ka-band: Frequency Re-use on Spot Beams
Frequency is re-used in non-adjoining spot beams to avoid interference
Frequency re-use is achieved by alternating the frequency sub-band and/or polarization used by each spot beam across coverage area
Frequency re-use increases the overall satellite capacity
Greatest commercial advantage

## Slide 28: Overcoming Propagation Delay in Current Bent Pipe Architectures
From Remote Site to AOC in
C4I Platforms
Site A
Site B
Gateway Station
AOC (C2 Center)
SATCOM
Fiber Optical Cable
Remote Site
2
1
3

## Slide 30: Attenuation caused by Rain Fade
Ka-band is great for MENA region as it receives less Rainfall leading to lesser attenuation

## Slide 31: Threats to Information Security
Major Threats
  Jamming
  Interception
  Spoofing
Counter Measures
  Transmission Security (Transec)
  Communication Security (Comsec)

## Slide 32: Overcoming threats to Information Security
COMSEC
Content protection Radio interface Authentication / confidentiality
NETSEC
Protection of signaling Transmitter authentication
TRANSEC
Protection of waveform Transmitter finding Receiver jamming
Network Layer
Data Link Layer
Physical Layer
Data Link Layer
Physical Layer
Physical Layer
Physical Security
OSI Model

## Slide 33: Overcoming threats to Information Security
TRANSEC
Protection of waveform from interception and direction to avoid receiver jamming, transmitter finding and access to radio signal.
Spread spectrum
Implemented at Physical Layer

## Slide 34: Overcoming threats to Information Security
COMSEC
Protection of information content by safeguarding authentication, confidentiality, integrity of signal and user data
Implemented at Physical, Data Link and Network layers
May be achieved through secure VPN or Cyber Protection Systems

## Slide 35: Regenerative Satellite System
Space Segment
Ground Segments
Rx
Demod
Tx
Site A
Site B
Uplink
Downlink
Packet Switch
Mod

## Slide 36: Regenerative Satellite
Uplink carrier is
      Demodulated to data packets,
      Rearranged on the basis of routing information
      Re-modulated onto downlink carrier
      Re-transmitted to the desired spot beam.
  Data from a particular beam can be transmitted to any beam by using satellite onboard switching
Improved (S/N) as data is regenerated which removes noise leading to higher throughput
Enabling on board satellite switching avoids Double Hop propagation delay for site to site communications
Very expensive satellite
Regenerative satellite is the latest trend in SATCOM technology with onboard switching and routing, enabling communications directly between terminals in a single hop without requiring a central hub.

## Slide 37: Bent Pipe versus Regenerative Satellites

## Slide 38: Conclusion
Communication is the fundamental component of C4I which is the key enabler of NCW
Optical fiber provides maximum bandwidth connectivity in (Tbps) but has lesser flexibility for remote deployment
Satellite is the best suited to provide interconnectivity, survivability and interoperability for remote and mobile setups due to easy deployment however it has limited bandwidth capacity and greater propagation delay.
Ka-band satellites provide greater throughput than C or Ku band Satellites
Most Ka-band satellites are base on Bent Pipe architecture whereby a double hop is needed to communicate between remote sites

## Slide 39: Conclusion cont’
The double hop in Ka-band (bent pipe) satellites may be avoided by providing fiber connectivity from Satellite Gateway to fixed sites (specially AOC) where possible.
Regenerative on Board Processing Ka satellites provides routing and switching on the satellite which enhances throughputs and avoids double hop propagation.
Regenerative Ka-band communication satellites are the new trend on SATCOM technology and will be the best suited for military use in C4I applications.
SATCOM is an essential requirements for C4I by:-
    Deployed tactical forces,
    Providing ideal continuity for operational services.
Standard Gigabit Ethernet (GE) interface as an open system architecture approach allows easy interconnectivity and interoperability to connect all C4I nodes.

## Slide 40: Any Questions?
Thank you